# SECTION 1: Identification of the substance/mixture and of the company/undertaking

# 1.1.	Product identifier

| Product form | : | Mixture |
| --- | --- | --- |
| Product name | : | Citra Shot |
| Product code | : | C-27 |

# 1.2.	Relevant identified uses of the substance or mixture and uses advised against

# 1.3.	Details of the supplier of the safety data sheet

EMPIRE INDUSTRIES

P.O. BOX 1404

BRENTWOOD, TN  37024

TELEPHONE 866.55EMPIRE or 615.315.0026
1.4.	Emergency telephone number

| Emergency number | : | CHEM TEL 800-255-3924 |
| --- | --- | --- |

SECTION 2: Hazards identification

# 2.1.	Classification of the substance or mixture

# GHS-US classification

| Flam. Liq. 4 | H227 |
| --- | --- |
| Skin Irrit. 2 | H315 |
| Skin Sens. 1 | H317 |

Full text of H-phrases: see section 16

# 2.2.	Label elements

# GHS-US labelling

| Hazard pictograms (GHS-US) | : | GHS07 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Signal word (GHS-US) | : | Warning |
| Hazard statements (GHS-US) | : | Combustible liquid Causes skin irritation May cause an allergic skin reaction |
| Precautionary statements (GHS-US) | : | Keep away from heat, sparks, open flames, No smoking. - No smoking Avoid breathing mist, spray, vapours Wash hands thoroughly after handling Contaminated work clothing must not be allowed out of the workplace Wear protective gloves, eye protection, face protection If on skin: Wash with plenty of Wash off with soap and plenty of water Specific treatment (see See first aid section of this material safety data sheet on this label) If skin irritation occurs: Get medical advice/attention If skin irritation or rash occurs: Get medical advice/attention Take off contaminated clothing and wash before reuse Take off contaminated clothing and wash it before reuse In case of fire: Use Suitable extinguishing media to extinguish Store in a well-ventilated place. Keep cool Dispose of contents/container to an approved waste disposal plant |

# 2.3.	Other hazards

No additional information available

# 2.4.	Unknown acute toxicity (GHS-US)

Not applicable

SECTION 3: Composition/information on ingredients

# 3.1.	Substance

Not applicable

# 3.2.	Mixture

| Name | Product identifier | % | GHS-US classification |
| --- | --- | --- | --- |
| D-limonene | (CAS No) 5989-27-5 | 90 - 95 | Flam. Liq. 3, H226 Skin Irrit. 2, H315 Skin Sens. 1, H317 Aquatic Acute 1, H400 Aquatic Chronic 1, H410 |

Full text of H-phrases: see section 16

# SECTION 4: First aid measures

# 4.1.	Description of first aid measures

| First-aid measures general | : | Never give anything by mouth to an unconscious person. If you feel unwell, seek medical advice (show the label where possible). |
| --- | --- | --- |
| First-aid measures after inhalation | : | Allow victim to breathe fresh air. Allow the victim to rest. |
| First-aid measures after skin contact | : | Rinse skin with water/shower. Wash with plenty of soap and water. Wash contaminated clothing before reuse. If skin irritation occurs: Gently wash with plenty of soap and water, Get medical advice/attention. Specific treatment (see first aid section on this label. on this label). |
| First-aid measures after eye contact | : | Rinse immediately with plenty of water. Obtain medical attention if pain, blinking or redness persist. |
| First-aid measures after ingestion | : | Rinse mouth. Do NOT induce vomiting. Obtain emergency medical attention. |

# 4.2.	Most important symptoms and effects, both acute and delayed

| Symptoms/injuries after inhalation | : | May cause an allergic skin reaction. |
| --- | --- | --- |
| Symptoms/injuries after skin contact | : | Causes skin irritation. |

# 4.3.	Indication of any immediate medical attention and special treatment needed

No additional information available

# SECTION 5: Firefighting measures

# 5.1.	Extinguishing media

| Suitable extinguishing media | : | Foam. Dry powder. Carbon dioxide. Water spray. Sand. |
| --- | --- | --- |
| Unsuitable extinguishing media | : | Do not use a heavy water stream. |

# 5.2.	Special hazards arising from the substance or mixture

| Fire hazard | : | Flammable liquid and vapour. |
| --- | --- | --- |
| Explosion hazard | : | May form flammable/explosive vapour-air mixture. |

# 5.3.	Advice for firefighters

| Firefighting instructions | : | Use water spray or fog for cooling exposed containers. Exercise caution when fighting any chemical fire. Prevent fire-fighting water from entering environment. |
| --- | --- | --- |
| Protection during firefighting | : | Do not enter fire area without proper protective equipment, including respiratory protection. |

# SECTION 6: Accidental release measures

# 6.1.	Personal precautions, protective equipment and emergency procedures

| General measures | : | Remove ignition sources. Use special care to avoid static electric charges. No open flames. No smoking. |
| --- | --- | --- |

# 6.1.1.	For non-emergency personnel

| Emergency procedures | : | Evacuate unnecessary personnel. |
| --- | --- | --- |

6.1.2.	For emergency responders

| Protective equipment | : | Equip cleanup crew with proper protection. |
| --- | --- | --- |
| Emergency procedures | : | Ventilate area. |

# 6.2.	Environmental precautions

Prevent entry to sewers and public waters. Notify authorities if liquid enters sewers or public waters.

# 6.3.	Methods and material for containment and cleaning up

| Methods for cleaning up | : | Soak up spills with inert solids, such as clay or diatomaceous earth as soon as possible. Collect spillage. Store away from other materials. |
| --- | --- | --- |

# 6.4.	Reference to other sections

See Heading 8. Exposure controls and personal protection.

# SECTION 7: Handling and storage

# 7.1.	Precautions for safe handling

| Additional hazards when processed | : | Handle empty containers with care because residual vapours are flammable. |
| --- | --- | --- |
| Precautions for safe handling | : | Wash hands and other exposed areas with mild soap and water before eating, drinking or smoking and when leaving work. Provide good ventilation in process area to prevent formation of vapour. No open flames. No smoking. Take precautionary measures against static discharge. Use only non-sparking tools. Avoid breathing mist, spray, vapours. |
| Hygiene measures | : | Always wash hands after handling the product. Contaminated work clothing should not be allowed out of the workplace. Wash contaminated clothing before reuse. |

# 7.2.	Conditions for safe storage, including any incompatibilities

| Technical measures | : | Proper grounding procedures to avoid static electricity should be followed. |
| --- | --- | --- |
| Storage conditions | : | Keep only in the original container in a cool, well ventilated place away from : Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. No smoking. Keep container tightly closed. |
| Incompatible products | : | Strong bases. Strong acids. |
| Incompatible materials | : | Sources of ignition. Direct sunlight. Heat sources. |

# 7.3.	Specific end use(s)

No additional information available

# SECTION 8: Exposure controls/personal protection

# 8.1.	Control parameters

| Citra Shot |
| --- |
| ACGIH | Not applicable |
| OSHA | Not applicable |

| D-limonene (5989-27-5) |
| --- |
| ACGIH | Not applicable |
| OSHA | Not applicable |

8.2.	Exposure controls

| Personal protective equipment | : | Safety glasses. Gloves. |
| --- | --- | --- |
| Hand protection | : | Wear protective gloves. |
| Eye protection | : | Chemical goggles or safety glasses. |
| Skin and body protection | : | Wear suitable protective clothing. |
| Respiratory protection | : | Wear appropriate mask. |
| Other information | : | Do not eat, drink or smoke during use. |

# SECTION 9: Physical and chemical properties

# 9.1.	Information on basic physical and chemical properties

| Physical state | : | Liquid |
| --- | --- | --- |
| Color | : | Orange |
| Odor | : | Citrus fruit |
| Odor threshold | : | No data available |
| pH | : | No data available |
| Melting point | : | No data available |
| Freezing point | : | No data available |
| Boiling point | : | 310 |
| Flash point | : | 145 |
| Relative evaporation rate (butylacetate=1) | : | No data available |
| Flammability (solid, gas) | : | No data available |
| Explosive limits | : | No data available |
| Explosive properties | : | No data available |
| Oxidising properties | : | No data available |
| Vapour pressure | : | No data available |
| Relative density | : | 0.85 |
| Relative vapour density at 20 °C | : | 4.9 |
| Solubility | : | Water: Solubility in water of component(s) of the mixture : • D-limonene: insoluble • Nonylphenoxypoly(ethyleneoxy)ethanol: soluble |
| Log Pow | : | No data available |
| Log Kow | : | No data available |
| Auto-ignition temperature | : | No data available |
| Decomposition temperature | : | No data available |
| Viscosity | : | No data available |
| Viscosity, kinematic | : | No data available |
| Viscosity, dynamic | : | No data available |

9.2.	Other information

No additional information available

# SECTION 10: Stability and reactivity

# 10.1.	Reactivity

No additional information available

# 10.2.	Chemical stability

Flammable liquid and vapour. May form flammable/explosive vapor-air mixture.

# 10.3.	Possibility of hazardous reactions

Not established.

# 10.4.	Conditions to avoid

Direct sunlight. Extremely high or low temperatures. Open flame. Overheating. Heat. Sparks.

# 10.5.	Incompatible materials

Strong acids. Strong bases.

10.6.	Hazardous decomposition products

Carbon monoxide. Carbon dioxide. May release flammable gases.

# SECTION 11: Toxicological information

# 11.1.	Information on toxicological effects

| Acute toxicity | : | Not classified |
| --- | --- | --- |

| D-limonene (5989-27-5) |
| --- |
| LD50 oral rat | 4400 mg/kg bodyweight (Rat; OECD 423: Acute Oral Toxicity – Acute Toxic Class Method; Literature study; > 2000 mg/kg bodyweight; Rat; Read-across) |
| LD50 dermal rabbit | > 5000 mg/kg bodyweight (Rabbit; Weight of evidence; Equivalent or similar to OECD 402) |
| ATE US (oral) | 4400.000 mg/kg bodyweight |

| Skin corrosion/irritation | : | Causes skin irritation. |
| --- | --- | --- |
| Serious eye damage/irritation | : | Not classified |
| Respiratory or skin sensitisation | : | May cause an allergic skin reaction. |
| Germ cell mutagenicity | : | Not classified |
| Carcinogenicity | : | Not classified |

| D-limonene (5989-27-5) |
| --- |
| IARC group | 3 - Not classifiable |

| Reproductive toxicity | : | Not classified |
| --- | --- | --- |
| Specific target organ toxicity (single exposure) | : | Not classified |

| Specific target organ toxicity (repeated exposure) | : | Not classified |
| --- | --- | --- |

| Aspiration hazard | : | Not classified |
| --- | --- | --- |

| Potential adverse human health effects and symptoms | : | Based on available data, the classification criteria are not met. |
| --- | --- | --- |
| Symptoms/injuries after inhalation | : | May cause an allergic skin reaction. |
| Symptoms/injuries after skin contact | : | Causes skin irritation. |

# SECTION 12: Ecological information

# 12.1.	Toxicity

| D-limonene (5989-27-5) |
| --- |
| LC50 fish 1 | 720 μg/l (LC50; OECD 203: Fish, Acute Toxicity Test; 96 h; Pimephales promelas; Flow-through system; Fresh water; Experimental value) |
| EC50 Daphnia 1 | 0.36 mg/l (EC50; OECD 202: Daphnia sp. Acute Immobilisation Test; 48 h; Daphnia magna; Static system; Fresh water; Experimental value) |
| Threshold limit algae 1 | 150 mg/l (EC50; OECD 201: Alga, Growth Inhibition Test; 72 h; Desmodesmus subspicatus; Static system; Fresh water; Read-across) |

# 12.2.	Persistence and degradability

| Citra Shot |
| --- |
| Persistence and degradability | Not established. |

| D-limonene (5989-27-5) |
| --- |
| Persistence and degradability | Readily biodegradable in water. Forming sediments in water. Adsorbs into the soil. Not established. |
| ThOD | 3.29 g O₂/g substance |

# 12.3.	Bioaccumulative potential

| Citra Shot |
| --- |
| Bioaccumulative potential | Not established. |

| D-limonene (5989-27-5) |
| --- |
| BCF fish 1 | 864.8 - 1022 (BCF; Pisces) |
| Log Pow | 4.38 (Experimental value; OECD 117: Partition Coefficient (n-octanol/water), HPLC method; 37 °C) |
| Bioaccumulative potential | Potential for bioaccumulation (4 ≥ Log Kow ≤ 5). Not established. |

# 12.4.	Mobility in soil

| D-limonene (5989-27-5) |
| --- |
| Log Koc | Koc,SRC PCKOCWIN v2.0; 1120 - 6324; QSAR |

12.5.	Other adverse effects

| Effect on the global warming | : | No known ecological damage caused by this product. |  |
| --- | --- | --- | --- |

| Other information | : | Avoid release to the environment. |
| --- | --- | --- |

# SECTION 13: Disposal considerations

# 13.1.	Waste treatment methods

| Waste disposal recommendations | : | Dispose in a safe manner in accordance with local/national regulations. |
| --- | --- | --- |
| Additional information | : | Handle empty containers with care because residual vapours are flammable. |
| Ecology - waste materials | : | Avoid release to the environment. |

# SECTION 14: Transport information

# Department of Transportation (DOT)

In accordance with DOT

Not regulated for transport

# Additional information

| Other information | : | No supplementary information available. |
| --- | --- | --- |

# ADR

No additional information available

Transport by sea

| Proper Shipping Name (IMDG) | : | TERPENE HYDROCARBONS, N.O.S. |
| --- | --- | --- |

Air transport

| Proper Shipping Name (IATA) | : | Terpene hydrocarbons, n.o.s. |
| --- | --- | --- |

# SECTION 15: Regulatory information

# 15.1. US Federal regulations

Citra Shot

Not listed on the United States TSCA (Toxic Substances Control Act) inventory

All components of this product are listed, or excluded from listing, on the United States Environmental Protection Agency Toxic Substances Control Act (TSCA) inventory

This product or mixture does not contain a toxic chemical or chemicals in excess of the applicable de minimis concentration as specified in 40 CFR §372.38(a) subject to the reporting requirements of section 313 of Title III of the Superfund Amendments and Reauthorization Act of 1986 and 40 CFR Part 372.

# 15.2. International regulations

# CANADA

No additional information available

# EU-Regulations

No additional information available

# Classification according to Regulation (EC) No. 1272/2008 [CLP]

No additional information available

# Classification according to Directive 67/548/EEC [DSD] or 1999/45/EC [DPD]

Not classified

National regulations

No additional information available

# 15.3. US State regulations

|  | California Proposition 65 - This product does not contain any substances known to the state of California to cause cancer and/or reproductive harm |
| --- | --- |

SECTION 16: Other information

| Revision date | : | 05/06/2015 |
| --- | --- | --- |
| Other information | : | None. |

| Full text of H-phrases: |
| --- |
| ------ | Aquatic Acute 1 | Hazardous to the aquatic environment — Acute Hazard, Category 1 |
| ------ | Aquatic Chronic 1 | Hazardous to the aquatic environment — Chronic Hazard, Category 1 |
| ------ | Flam. Liq. 3 | Flammable liquids, Category 3 |
| ------ | Flam. Liq. 4 | Flammable liquids, Category 4 |
| ------ | Skin Irrit. 2 | Skin corrosion/irritation, Category 2 |
| ------ | Skin Sens. 1 | Sensitisation — Skin, category 1 |
| ------ | H226 | Flammable liquid and vapour |
| ------ | H227 | Combustible liquid |
| ------ | H315 | Causes skin irritation |
| ------ | H317 | May cause an allergic skin reaction |
| ------ | H400 | Very toxic to aquatic life |
| ------ | H410 | Very toxic to aquatic life with long lasting effects |

| NFPA health hazard | : | 1 - Exposure could cause irritation but only minor residual injury even if no treatment is given. |  |
| --- | --- | --- | --- |
| NFPA fire hazard | : | 1 - Must be preheated before ignition can occur. |  |
| NFPA reactivity | : | 1 - Normally stable, but can become unstable at elevated temperatures and pressures or may react with water with some release of energy, but not violently. |  |

| HMIS III Rating |
| --- |
| Health | : | 2 Moderate Hazard - Temporary or minor injury may occur |
| Flammability | : | 2 Moderate Hazard - Materials which must be moderately heated or exposed to high ambient temperatures before ignition will occur. Includes liquids having a flash point at or above 100 F but below 200 F. (Classes II & IIIA) |
| Physical | : | 1 Slight Hazard - Materials that are normally stable but can become unstable (self-react) at high temperatures and pressures. Materials may react non-violently with water or undergo hazardous polymerization in the absence of inhibitors. |
| Personal Protection | : | B |
| Personal Protection |  | B - Safety glasses, Gloves |

SDS US (GHS HazCom 2012)

No representation or warranty, either expressed or implied, of merchantability, fitness for a particular purpose, or of any other nature, is made with respect to information concerning the product referred to in this document.  The information contained herein is, to the best of our knowledge and belief, accurate.  However, since the conditions of handling and use are beyond our control, it is impossible to foresee every health effect or exposure risk incurred by the use of this product.  All chemicals present some degree of hazard and should be used with caution.  The information and recommendations contained herein are presented in good faith.  The user should review this information in conjunction with their knowledge of the application intended to determine the suitability of this product for such purpose.  In no event will the supplier be responsible for any damages of any nature whatsoever, resulting from the use, reliance upon, or the misuse of this information.  Furthermore, it is the direct responsibility of the user to comply with all applicable regulations governing the use and disposal of this material.